# Microcontroller fire alarm system
Check capacitor size.
## Microcontroller pin layout
The pin layout of the PICAXE microcontroller is given by the following image. Any pin numbers used throughout this document are in reference to this diagram.

## Language used in this document
The following definitions apply to the vocabulary used within this document.
If one of the bellow terms is written in italics, then it is referring to the definitions bellow. However, if there is text that is not italic in which one of these definitions is used it is up to reader discretion whether if refers to the bellow definitions, though most of the time it will not.
#### High
In the context of referring to a voltage the term high is defined as 5V±1V.
#### Low
In the context of referring to a voltage the term low is defined as 0V±1V.
#### Override switch
In the context of referring to an input for the PICAXE microcontroller the term override switch is defined as pin 18 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term override switch is defined as PORT A bit 1.
#### Sensor one
In the context of referring to an input for the PICAXE microcontroller the term sensor one is defined as pin 17 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one is defined as PORT A bit 0.
#### Sensor two
In the context of referring to an input for the PICAXE microcontroller the term sensor two is defined as pin 16 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two is defined as PORT A bit 7.
#### Sensor three
In the context of referring to an input for the PICAXE microcontroller the term sensor three is defined as pin 15 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three is defined as PORT A bit 6.
#### Alarm
In the context of referring to an output for the PICAXE microcontroller the term alarm is defined as pin 6 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term alarm is defined as PORT B bit 0.
#### Sensor one indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor one indicator is defined as pin 7 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one indicator is defined as PORT B bit 1.
#### Sensor two indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor two indicator is defined as pin 8 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two indicator is defined as PORT B bit 2.
#### Sensor three indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor three indicator is defined as pin 9 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three indicator is defined as PORT B bit 3.
#### Sensor one sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor one sprinkler is defined as pin 10 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one sprinkler is defined as PORT B bit 4.
#### Sensor two sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor two sprinkler is defined as pin 11 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two sprinkler is defined as PORT B bit 5.
#### Sensor three sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor three sprinkler is defined as pin 12 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three sprinkler is defined as PORT B bit 6.
#### Triggered
In the context of referring to sensor one, sensor two, or sensor three the term triggered is defined as the mentioned sensor being high for 500±100ms. Furthermore, if the mentioned sensor continues to be high for over 500±100ms, then it will only count as a single instance of being triggered, regardless of how long the mentioned sensor is high for.
#### The Outputs
In the context of referring to output pins from the PICAXE microcontroller, the term the outputs is defined as alarm, sensor one indicator, sensor two indicator, sensor three indicator, sensor one sprinkler, sensor two sprinkler, & sensor three sprinkler.
## System Planning

### Problem
Ask sir what they mean by “evidence”
A small office is in need of a fire alarm & sprinkler system, as the office needs to comply with fire safety regulations. Furthermore, there are valuable prototypes of products that are stored in side the office, which would be destroyed in the event of a fire. An alarm & sprinkler system would stop the fire from the destroying the products.
### Specification
At least 3 qualitative and 3 quantitative system specifications (six total).
At least 2 Electronic parameters (e.g. time, frequency, current, voltage, power), including tolerances.
Ask sir if any of these count as “the wordy one” requirements, as all feedback has lead to me defining specifications with exact definitions.
Specifications:
1) While the override switch is high the outputs will be forced low.
2) When sensor one indicator is high, the sensor one sprinkler will be high.
3) When sensor two indicator is high, the sensor two sprinkler will be high.
4) When sensor three indicator is high, the sensor three sprinkler will be high.
5) When sensor one is triggered then the LED associated to sensor one indicator will be illuminated.
6) When sensor two is triggered then the LED associated to sensor two indicator will be illuminated.
7) When sensor three is triggered then the LED associated to sensor three indicator will be illuminated.
8) When sensor one is triggered the alarm will be high.
9) When sensor two is triggered the alarm will be high.
10) When sensor three is triggered the alarm will be high.
11) After the override switch has been released (set low), sensor one, sensor two, & sensor three can be triggered again.
12) Non-consecutive high on sensor one, sensor two, & sensor three will reset the time taken for the corresponding sensor to be triggered.
## System Development

### Flowchart
Produce a flowchart that is clearly annotated & shows the structure of the program.

1: This is the start of the program.
2: This checks if the override switch is high, if it is not then sensor one, sensors two, & sensor three will be checked. If it has then it will return back to the start after executing other relevant instructions without passing through the checks for sensor one, sensor two, & sensor three so they cannot be triggered.
3: Checks if sensor one has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
4: Checks if sensor two has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
5: Checks if sensor three has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
6: This stops any ongoing alarms by setting the alarm to low.
7: This stops any ongoing sprinklers by setting sensor one sprinkler, sensor two sprinkler, & sensor three sprinkler to low.
8: This turns off any illuminated indicator LEDS by setting sensor one indicator, sensor two indicator, & sensor three indicator to low.
9: This turns on the sensor one sprinkler by setting it to high.
10: This turns on the alarm by setting it to high.
11: This turns on the sensor two sprinkler by setting it to high.
12: This turns on the sensor three sprinkler by setting it to high.
13: This turns on the sensor one indicator by setting it to high.
14: This turns on the sensor two indicator by setting it to high.
15: This turns on the sensor three indicator by setting it to high.
### Code Description
At simplistic level the code can be thought of as checking if sensor one, sensor two, or sensor three has been triggered. And setting the appropriate outputs (sensor one indicator & sensor one sprinkler/sensor two indicator & sensor two sprinkler/sensor three indicator & sensor three sprinkler) & alarm to high. Unless the override switch has been pressed, which forces the outputs to low.

Before describing the code structure, there are a few variables, which are defined in the “vars” label used throughout the code that will be explained.
The “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count” all keep track of the number of consecutive cycles that sensor one, sensor two, & sensor three, have been triggered respectively.
The “Result” variable is used to temporarily store the result of calculations when the working register is overwritten by other operations before the calculation result is needed.

At a deeper level, the code executed by the PICAXE microcontroller performs what will be referred to as a cycle every 100±20ms. Before the first cycle, basic initialisation & variable definitions are executed. After that, cycles are continuously executed until the PICAXE microcontroller stops receiving input power (on pin 14).
A cycle consists of:
1) Checking if the override switch is high.
2) Checking if sensor one is high.
3) Checking if sensor two is high.
4) Checking if sensor three is high.
5) Handling non-consecutive increments of “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count”
6) Waiting for 100ms.
7) Going back to step 1.

Each stage will be expanded upon bellow.
#### Stage One
In stage one the code checks whether the override switch switch is high. If the override switch is high, then the code sets all of PORTB to low & resets “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count” to 0. This will stop any alarms, indicators, & sprinklers that might be connected to the outputs, which is where the “override switch” gets its name from. It overrides any other outputs.
Furthermore, after doing this it directly goes to the start of the cycle again, skipping any checks for sensor one, sensor two, & sensor three. This ensures that the outputs must remain low when the override switch is high.
#### Stage Two
In stage two the code checks whether sensor one is high. If it is low, then the subroutine exits early and the code moves onto stage three. If it is high then it checks if “Sprinkler_One_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor one indicator, & sensor one sprinkler are set high. If it has a value less then five, the “Sprinkler_One_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_One_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Three
In stage three the code checks whether sensor two is high. If it is low, then the subroutine exits early and the code moves onto stage four. If it is high then it checks if “Sprinkler_Two_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor two indicator, & sensor three sprinkler are set high. If it has a value less then five, the “Sprinkler_Two_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_Two_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Four
In stage four the code checks whether sensor three is high. If it is low, then the subroutine exits early and the code moves onto stage five. If it is high then it checks if “Sprinkler_Three_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor three indicator, & sensor three sprinkler are set high. If it has a value less then five, the “Sprinkler_Three_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_Three_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Five
Using bit checks on sensor one, sensor two, & sensor three the PICAXE microcontroller checks if any of them are high or low. If the input is low then the associated sprinkler count is set to 0. This prevents occasional voltage spikes on sensor one, sensor two, and/or sensor three from eventually incrementing the associated sprinkler count to 5. However, if the input is high, then no action is taken. This only allows the associated sprinkler count for a sensor to reach 5 if the sensor has been measured as high for 500±100ms (five cycles).
#### Stage Six
The PICAXE microcontroller then sleeps for 100±20ms, by calling the subroutine “wait100ms”. This allows for the time cycle will take to be known & therefore how long it will take for sensor one, sensor two, and/or sensor three to be triggered.
#### Stage Seven
The code goes back to stage one & continues to repeat cycles indefinitely.

### Code
;*******************************************************************
; TEMPLATE PROVIDED BY CENTRE FOR USE WITH HEADER FILE
;
; TITLE: #### Microcontroller fire alarm system #####
; AUTHOR: ######## Tye #########
; DATE: ####### 2024/10/14 ######
;

;******************************************************************
; PROGRAM DESCRIPTION:
;
; #### Checks if a fire has started & triggers alarms & sprinklers in response #######
;
;******************************************************************

;*********************************************************************
; DEFINITIONS
;*********************************************************************
;The header file can be used with either the PIC16F88 or PIC16F877A
;#define UseRC	; UseRC, UseCrystal or UseInternal - defaults to UseRC
#define UseInternal	; UseRC, UseCrystal or UseInternal - defaults to UseRC
#define UseInterrupt
;#define Watchdog	; The Watchdog timers are off by default unless this is uncommented

;#include "Header.inc" ;Predefined wait subroutines - wait1ms, wait10ms, wait100ms, wait1000ms
;Predefined ADC subroutines - readadc0, readac1, readadc2
;	radix	dec ; set default number radix to decimal
;radix	hex	; set default number radix to hex

;*********************************************************************
; VARIABLES
;*********************************************************************

; #### Create any variables here using the EQU statement
;
;
; #### e.g.	myVar equ b1

;*********************************************************************
; MAIN PROGRAM
;*********************************************************************

; ---------- Initialisation ----------
init:
; Clears inputs & outputs
clrf PORTB
clrf PORTA

bsf STATUS,RP0 ; Allows writing to TRISx (memory page 1)

; Sets B.x Output
movlw h'00'
movwf TRISB
; Sets A.x Input
movlw h'FF'
movwf TRISA

bcf STATUS,RP0 ; Locks TRISx (memory page 0)

vars:
; Stores how many times each spinkler has been triggered
Sprinkler_One_Count EQU B0
Sprinkler_Two_Count EQU B1
Sprinkler_Three_Count EQU B2

; Stores the result of calculations
Result EQU B3

; Init all vars to 0
movlw h'0'
movwf Sprinkler_One_Count
movwf Sprinkler_Two_Count
movwf Sprinkler_Three_Count
movwf Result

; ---------- Main Cycle ----------
main:
; Test for override.
btfsc PORTA, 0
goto override_switch

; Run spinklers
btfsc PORTA, 1
call spk_one_guard
btfsc PORTA, 2
call spk_two_guard
btfsc PORTA, 3
call spk_three_guard

; Reset spk counts (if appropriate)
btfss PORTA, 1
call zero_spk_one_count
btfss PORTA, 2
call zero_spk_two_count
btfss PORTA, 3
call zero_spk_three_count

; Wait for awhile
call wait100ms

goto main

; ---------- Override Switch ----------
override_switch:
clrf PORTB

; Reset counts for spinkler triggers
movlw h'00'
movwf Sprinkler_One_Count
movwf Sprinkler_Two_Count
movwf Sprinkler_Three_Count
goto main

; ---------- Sprinkler One ----------
spk_one_guard:
; Set Result 0 if count is not 5.
btfss Sprinkler_One_Count, 0
bsf Result, 0
btfss Sprinkler_One_Count, 2
bsf Result, 0

; Increment in place if bellow 5.
btfsc Result, 0
incf Sprinkler_One_Count, 1

; Trigger if 5.
btfss Result, 0
call spk_one_trigger

bcf Result, 0 ; Reset Result reg.
return

spk_one_trigger:
; Trigger,
bsf PORTB, 0 ; Alarm
bsf PORTB, 1 ; Sensor one indicator
bsf PORTB, 4 ; Sensor one sprinkler
return

; ---------- Sprinkler Two ----------
spk_two_guard:
; Set Result 0 if count is not 5.
btfss Sprinkler_Two_Count, 0
bsf Result, 0
btfss Sprinkler_Two_Count, 2
bsf Result, 0

; Increment in place if bellow 5.
btfsc Result, 0
incf Sprinkler_Two_Count, 1

; Trigger if 5.
btfss Result, 0
call spk_two_trigger

bcf Result, 0 ; Reset Result reg.
return

spk_two_trigger:
; Trigger,
bsf PORTB, 0 ; Alarm
bsf PORTB, 2 ; Sensor two indicator
bsf PORTB, 5 ; Sensor two sprinkler
return

; ---------- Sprinkler Three ----------
spk_three_guard:
; Set Result 0 if count is not 5.
btfss Sprinkler_Three_Count, 0
bsf Result, 0
btfss Sprinkler_Three_Count, 2
bsf Result, 0

; Increment in place if bellow 5.
btfsc Result, 0
incf Sprinkler_Three_Count, 1

; Trigger if 5.
btfss Result, 0
call spk_three_trigger

bcf Result, 0 ; Reset Result reg.
return

spk_three_trigger:
; Trigger,
bsf PORTB, 0 ; Alarm
bsf PORTB, 3 ; Sensor three indicator
bsf PORTB, 6 ; Sensor three sprinkler
return

; ---------- Count Resets ----------
zero_spk_one_count:
movlw h'00'
movwf Sprinkler_One_Count
return
zero_spk_two_count:
movlw h'00'
movwf Sprinkler_Two_Count
return
zero_spk_three_count:
movlw h'00'
movwf Sprinkler_Three_Count
return

;*********************************************************************
;	INTERRUPT SERVICE ROUTINE
;*********************************************************************

W_SAVE	EQU B20 ; backup registers used in interrupts

interrupt:
movwf	W_SAVE	; Copy W to save register
    btfss INTCON,INT0IF	; check correct interrupt has occurred
    retfie	; no, so return and re-enable GIE

;**********The interrupt service routine (if required) goes here*********

   bcf INTCON,INT0IF	; bit clear so clear interrupt flag

movf W_SAVE,W	; restore W
retfie ; return and re-set GIE bit

    END ; all programs must end with this

### Commands Used
Including at least 10 different commands as well as conditional & unconditional branching.
1: “clrf”
2: “bsf”
3: “movlw”
4: “movwf”
5: “bcf”
6: “equ”
7: “btfsc”
8: “goto”
9: “call”
10: “btfss”
11: “incf”
12: “return”
### Assembling
Full record of assembling the program (include screen shot). Include finding & fixing syntax errors.
When defining the registers that are used to store how many times each sensors has been set, I mistakenly used the same name for each register.
I fixed this by changing each name to unique ones.

When I was working on the override switch functionality, I accidentally typed “btfsc PORTA 0” instead of “btfsc PORTA, 0”. This resulted in the following syntax error.
I easily fixed this by changing it to “btfsc PORTA, 0”

During implementing the sensor one subroutine, I was attempting to store the result of a calculation into the W register, & I got a syntax error when trying to do that with this instruction.

I wasn’t entirely sure why there was an issue with performing btfs* operations on the W register, other than for the reason that it is the working register. To circumnavigate this problem I created another registered to move the value into before checking it.

This allowed the program to compile without an issue.

I made a typo when refering to the “Sprinkler_One_Count” register whilst rewritting my sprinkler subroutine. I easily fixed this by correcting the typo.

I made a mistake of calling a subroutine with “goto” instead of “call”, which resulted in a “Stack Underflow” error when I was testing it.
I easily fixed this by changing the “goto” to a “call” instruction.
## System Realisation

### Block Diagram

### Circuit Diagram
The diagrams had to be split into two images (a top & a bottom half) due to limitations with the software I was using.
#### Testing Configuration
This is the configuration of the circuit I will use to test that the entire system is functioning within the specification.

#### Deployed Configuration
This is the configuration of the circuit that will be used by customers when they install the system.

### Components List
Capacitor
- 1x PICAXE microcontroller
- 4x Push to make switches
- 7x LED
- 7x 330Ω resistors
- 4x 10kΩ resistors
- 3x 100kΩ resistors
### Photo Of Circuit
Needs to be very well organised, with all wires horizontal or vertical.

### Evidence of Downloaded Program
#### Downloading Data

#### Downloading Program

#### Successfully Installed

### Test Plan

Override switch, sensor one, sensor two, sensor three, are to be assumed low unless explicitly stated otherwise.
Between each test the override switch should be pressed for at least 500±100ms.
Specification	Test	Why	Expected Result	Actual Result
2, 5, 8	Have sensor one high for over 500ms	To test if sensor one works as expected.	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – x / Sensor one indicator – x / Sensor one sprinkler – x
3, 6, 9	Have sensor two high for over 500ms	To test if sensor two works as expected.	The following outputs will be high: alarm, sensor two indicator, sensor two sprinkler	Alarm – x / Sensor two indicator – x / Sensor two sprinkler – x
4, 7, 10	Have sensor three high for over 500ms	To test if sensor three works as expected.	The following outputs will be high: alarm, sensor three indicator, sensor three sprinkler	Alarm – x / Sensor three indicator – x / Sensor three sprinkler – x
12	Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms	To test that the sensor won’t trigger due to non-consecutive inputs.	All of the outputs will be low.	Alarm – x / Sensor one indicator – x / Sensor one sprinkler – x / Sensor two indicator – x / Sensor two sprinkler – x / Sensor three indicator – x / Sensor three sprinkler – x
2, 3, 4, 5, 6, 7, 8, 9, 10	Have sensor one, sensor two, & sensor three high for over 500ms	If all of the corresponding sensor outputs will be triggered along with the alarm	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler, sensor two indicator, sensor two sprinkler, / sensor three indicator, sensor three sprinkler	Alarm – x / Sensor one indicator – x / Sensor one sprinkler – x / Sensor two indicator – x / Sensor two sprinkler – x / Sensor three indicator – x / Sensor three sprinkler – x
1	Have sensor one high for 1000ms & the override switch high for the duration of the test	If the override switch stops the sensors from triggering	All of the outputs will be low.	Alarm – x / Sensor one indicator – x / Sensor one sprinkler – x / Sensor two indicator – x / Sensor two sprinkler – x / Sensor three indicator – x / Sensor three sprinkler – x
11	Have the override switch & sensor one high initially. When the test starts set override switch low. Then keep sensor one high for 1000ms	If the sensors can re-trigger after they have been overridden	500±100ms after the override switch has been released the following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – x / Sensor one indicator – x / Sensor one sprinkler – x

TESTED PICTURES WITHOUT INPUTS CONNECTED – MAKE ARGUMENT OF NOT WANTING ANY INPUTS TO INTERFERE
Add error of +- 0.005
All high test:
With input voltage of 4.86V
B.0 = 4.09V
B.1 = 4.19V
B.2 = 4.10V
B.3 = 4.00V
B.4 = 4.31V
B.5 = 4.13V
B.6 = 4.20V
All Low Test:
With input voltage of 5.01V
B.0 = 0.01V
B.1 = 0.01V
B.2 = 0.02V
B.3 = 0.02V
B.4 = 0.01V
B.5 = 0.01V
B.6 = 0.02V
### Test Equipment Circuit Diagram

### Results From Test

### Analysis Of Test Results
Compare results to the flowchart & explain what this means in regards to the flowchart & system function.

## Evaluation

### Progress & Performance
Reflect upon the progress & performance

### Reliability
How consistently/well did the system work?

### Comparison
Compare the test results with the initial specification. Use a table

### Improvements
At least 2 suggestions for improvement to the system alongside how they will improve the system.