## System Planning
Name:
ID:
DURING TESTING REPLACED ANALOGUE IN SWITCHES WITH WIRES
### Problem
What, why, who, where.
Research of a specific example.
Alice is a mum to her 5 year old daughter (Jessie). Alice is helping Jessie to learn how to add numbers together at home to help her get ahead in primary school. However, Alice is often busy and cannot always supervise Jessie and check her work.
Jessie finds using calculators to be unintuitive and hard, as she finds it easier to understand analogue systems. My adder system will help Alice by allowing Jessie to check her if she added two numbers together correctly, especially as the inputs are both analogue, allowing Jessie to comprehend it easier.
Other calculators available, such as the “aristotle-calculator”[1], have multiple buttons that with advanced features such as adding and subtracting values from the calculator memory. These extra buttons can cause an issue when they are accidentally pressed, which will confuse Jessie. Compounding these issues, the calculator allows for inputs of multiple digits potentially causing Jessie to feel overwhelmed, as she is only just learning to work with small numbers.
[1] : https://www.ukprinting.com/aristotle-calculator
My adder does not have these issues, as it can only add small numbers together, making it more appropriate for a first introduction to addition.
### Specification
At least 4 qualitative and 4 quantitative system specifications (a list of 8).
Electronic parameters (e.g. time, frequency, current, voltage, power (inc. tolerances)
1) The sum of the two analogue inputs will be displayed by the seven segment display.
2) The user will have the option to see the value of analogue each input separately.
3) The numbers from and including 0 to 15 can be displayed as output.
4)
5) The voltage range for each analogue input will be between -5.0±0.1V and 0.0±0.1V.
6)
7)
8)
## System Development
Have at least 3 alternate sub-system/circuits
### Analogue Input Sub-System
This Sub-System is responsible for converting user input into an analogue voltage between -5±0.1V and 0±0.1V using potentiometers. The reason for this voltage range is that the Mixer Sub-System (on page 4) will invert the input voltage. Since the initial voltage is negative, the voltage output will be positive.
Additionally, push-to-break switches are placed between each potentiometer, allowing for the user to disable either input to see the value of the other input. Push-to-break switches are used instead of push-to-make, because I want the default behaviour to be showing the sum of the values. Furthermore, the user would have to hold down both buttons to see the desired output, which is not a good user experience.
#### Circuit Diagram

#### Test Diagram

#### Test Table
Each test only list the expected values for components relevant to the test.
Test Number	Switch Position	Expected Output / V	Measured Output / V
1	One: Closed	Analogue One: 0±0.1 / Pot One: 0±0.1	Analogue One: 0.00±0.005 / Pot One: 0.00±0.005
2	Two: Closed	Analogue Two: 0±0.1 / Pot Two: 0±0.1	Analogue Two: 0.00±0.005 / Pot Two: 0.00±0.005
3	One: Closed	Analogue One: -5±0.1 / Pot One: -5±0.1	Analogue One: -4.96±0.005 / Pot One: -4.96±0.005
4	Two: Closed	Analogue Two: -5±0.1 / Pot Two: -5±0.1	Analogue Two: -4.99±0.005 / Pot Two: -4.99±0.005
5	One: Open	Analogue One: 0±0.1 / Pot One: -5±0.1	Analogue One: 0.00±0.005 / Pot One: -4.96±0.005
6	Two: Open	Analogue Two: 0±0.1 / Pot Two: -5±0.1	Analogue Two: 0.00±0.005 / Pot Two: -4.99±0.005

#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust potentiometer one (VR2) / potentiometer two (VR1) until Pot One / Pot Two displays the value expected.
3) Measure and record the value of Analogue One and Pot One / Analogue Two and Pot Two.
4) Repeat from step 2 for all the tests.
#### Test Review
The testing of this sub-system went well, with no issues during testing and all tests producing outputs that are within the desired tolerance range (shown in the Test Table). However, at the time of testing I had to substitute both push to break switches with push to make switches due there being no push to break switches available at the time of testing. This did not impact the execution of the test, as in the “switch position” column it states whether a switch is open or closed, which produces the same behaviour with both push to break and push to make switches.
The largest outlier was the minimum voltage output from Pot One, with it being +0.04V from the expected output in tests 3 and 5, however it was still within specification as the maximum allowed voltage within tests 3 and 5 is -4.90V.
### Mixer Sub-System
The mixer (also known as a summing amplifier) is responsible for combining the two analogue inputs into a single analogue voltage.
The mixer has a gain of -1[2] for both inputs, because I do not want to amplify the two inputs, only combine them together.
[2] G = frac {-R_f} {R_"in"} = frac { -1KΩ } { 1KΩ } = -1
In the original design of this sub-system, I was using 5V and 0V for the positive and negative supply of the op amp respectively. However, I was unsure if these values would allow the mixer to output a suitable voltage range, as the op amp could possibly saturate before reaching either value. After testing the positive and negative saturation of the op amp using 5V and 0V, it had a range much smaller than initially expected. I solved the issue by changing the supply voltages to 12V and -5V, which solved this issue, allowing for a much larger voltage range.
#### Circuit Diagram

#### Test Diagram

#### Test Table
The expected outcome of the test is predicted using the equation: V_{out} = R_{f} ( {frac { V_{1} } {R_{1}}} + frac {V_{2}} {R_{2}} ) , where V_{ 1 } is analogue input one, V_{ 2 } is analogue input two, and R_{f} R_{ 1 } R_{ 2 } are at 1±0.025KΩ.
Test Number	Test Inputs / V	Expected Outcome / V	Measured Outcome / V
1	Analogue One: 0±0.04 / Analogue Two: 0±0.04	Mixer Output: 0±0.04	Mixer Output: 0.00±0.005
2	Analogue One: -2±0.04 / Analogue Two: 0±0.04	Mixer Output: 2±0.04	Mixer Output: 2.01±0.005
3	Analogue One: 0±0.04 / Analogue Two: -2±0.04	Mixer Output: 2±0.04	Mixer Output: 2.01±0.005
4	Analogue One: -2±0.04 / Analogue Two: -2±0.04	Mixer Output: 4±0.04	Mixer Output: 4.01±0.005
5	Analogue One: -4±0.04 / Analogue Two: -4±0.04	Mixer Output: 8±0.04	Mixer Output: 8.02±0.005

#### Test procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust the potentiometer for Analogue One until the voltage measured from Analogue One In is at the required voltage for the test.
3) Adjust the potentiometer for Analogue Two until the voltage measured from Analogue Two In is at the required voltage for the test.
4) Measure & record the voltage from Mixer Output.
5) Repeat from step 2 for all the tests.
#### Test Review
Went well with no issues.
### Resistor Ladder Sub-System
#### Circuit Diagram
The purpose of R17 (8.2KΩ) is to cause the Overflow voltage to be at about 8V, because this is the highest voltage output tested for the Mixer Sub-System.
Ideally R17 would have a resistance of exactly 8KΩ, which would cause the output of Overflow to be exactly at 8V. However, closest E24 resistance to 8KΩ is 8.2KΩ, so I have to use an 8.2KΩ resistor for R17. This causes the Overflow voltage to be 7.93V, which is calculated by:
V_{ Overflow } = frac {R_{1..16} times V_{"in"}} {R_{1..16} + R_{17}} = frac {"16K" times 12} {"16K" times "8.2K"} = "7.93V"
The value of R17 being 8.2KΩ rather than 8KΩ does not effect the overall function of the system, so I have decided that the measured output values will be compared against the values predicted using the 8.2KΩ resistor.
#### Test Diagram

#### Test Table
The Expected Output for each test is calculated using the formula V_{ out } = frac { R_{2} times V_{ "in" } } {R_{2} times {R_{1}}} where:
R_{ 2 } = The total resistance from the 12V in to the measured output.
R_{ 1 } = The total resistance from the 0V out to the measured output.
V_{ "in" } = 12V.
V_{ out } = The expected output voltage.
Test Number	Expected Output	Measured Output
1	Overflow: 7.93±0.1V	Overflow: 7.95±
2	Z: 7.44±0.05V	Z: 7.44±
3	Y: 6.94±0.05V	Y: 6.94±
4	X: 6.45±0.05V	X: 6.44±
5	W: 5.95±0.05V	W: 5.95±
6	V: 5.45±0.05V	V: 5.45±
7	U: 4.96±0.05V	U: 4.96±
8	T: 4.46±0.05V	T: 4.46±
9	S: 3.97±0.05V	S: 3.97±
10	R: 3.47±0.05V	R: 3.46±
11	Q: 2.98±0.05V	Q: 2.97±
12	P: 2.48±0.05V	P: 2.48±
13	O: 1.98±0.05V	O: 1.98±
14	N: 1.49±0.05V	N: 1.49±
15	M: 0.99±0.05V	M: 0.99±
16	L: 0.50±0.05V	L: 0.49±
17	R34: 8.2±0.205KΩ	R34: 8.09±0.005KΩ

#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Measure and record the required outputs for each test.
#### Test Review
Very well, no issues.
### Comparator Chain Sub-System
Originally, each op amp had a V+ of 5V and a V- of 0V, however, this supply voltage range was too small for the op amps to function correctly, with voltage inputs from 1V to 0V and voltages above 5V producing unreliable results. I solved this by changing the V+ to 12V and V- to -5V, this allowed the op amps to produce correct results within the 0V to 8V range output by the Resistor Ladder Sub-System.
#### Circuit Diagram

#### Test Diagram

#### Test Table
The expected voltage range is calculated from the Resistor Ladder Sub-System on page 6. However, the expected results had to be adjusted, as the 12V output from my power supply gave an output of 12.10V. This disproportionally effected the tests 12 to 17 if this was not taken into account.
Test Number	Comparator Outputs	Expected V_{ ref } Range / V ±0.05	Measured V_{ ref } Range / V
1	All: -4±1V	0.00 to 0.50	0.00 to 0.50
2	L: 10±1V	0.50 to 1.00	0.51 to 0.97
3	L, M: 10±1V	1.00 to 1.50	0.98 to 1.49
4	L to N: 10±1V	1.50 to 2.00	1.49 to 2.03
5	L to O: 10±1V	2.00 to 2.50	2.04 to 2.52
6	L to P: 10±1V	2.50 to 3.00	2.53 to 3.01
7	L to Q: 10±1V	3.00 to 3.50	3.02 to 3.50
8	L to R: 10±1V	3.50 to 4.00	3.51 to 4.00
9	L to S: 10±1V	4.00 to 4.50	4.01 to 4.49
10	L to T: 10±1V	4.50 to 5.00	4.50 to 4.99
11	L to U: 10±1V	5.00 to 5.50	5.00 to 5.48
12	L to V: 10±1V	5.50 to 6.00	5.49 to 6.04
13	L to W: 10±1V	6.00 to 6.50	6.05 to 6.54
14	L to X: 10±1V	6.50 to 7.00	6.55 to 7.05
15	L to Y: 10±1V	7.00 to 7.50	7.05 to 7.55
16	L to Z: 10±1V	7.50 to 8.00	7.55 to 8.04
17	L to Overflow: 10±1V	8.00 to 9.00	8.05 to 9.00

#### Test Procedure
1) Set up the circuit as shown in the test diagram.
2) Ensure that the inputs “Overflow, Z, Y, X, W, V, U, T, S, R, Q, P, O, N, M, and L” are set at the corresponding voltage from the Resistor Ladder Sub-System Test Table on page 7, and that they maintain this voltage throughout the test.
3) Any outputs not mentioned in “Comparator Outputs” for a test are expected to have an output of -4±1V for the corresponding test.
4) For each test, measure and record the lowest V_{ ref } that produces the same output from the op amps as listed in “Comparator Outputs”. Then measure and record the highest V_{ ref } that produces the same output. Combining both these measurements into a range where the op amps output the desired values.
V_{ ref } must not be adjust beyond the range 0V to 9V.
5) Repeat step four for every test.
#### Test Review
All the tests went well, with the measured range aligning with the expected range within the tolerances. Tests 15, 16, and 17, came close to failing, with the measured voltage range being at the maximum tolerance for the expected voltage range. A large contributor to this deviance can be assigned to the ±5% tolerance of each resistor within the Resistor Ladder Sub-System.
#### Interface issues
When I connected the Mixer output, all the comparitor outputs were at 4±1V, even when the Vref signal was at 0V.
When Vref was under 1.5V, all op amp high
When Vref above 1.5V op amps worked, but switched when X Y Z Ov switched on at Vref > ~5.25V

### Priority Encoder Sub-System
The Priority Encoder Sub-System originally output a binary signal, which was going to be converted into a BCD signal by the Seven Segment Display Sub-System before being converted into the seven segment display format. However, I was not able to acquire the required chip (SN74184), which would have done the conversion from binary to BCD, due to supply shortages. Because of this I had to redesign this sub-system to output a BCD signal, making the binary to BCD conversion redundant.
The original binary priority encoder can be seen at Alternative Sub-Systems Priority Encoder Binary on page 17.
#### Truth Table
Encoder In / ±1V					BCD Out / Logic					10’s
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		E	D	C	B	A
-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	0		0
10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	1		1
10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	1	0		2
10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	1	1		3
10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	0	0		4
10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	0	1		10
10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	1	0		6
10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	1	1		7
10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4		0	1	0	0	0		8
10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4		0	1	0	0	1		9
10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4		1	0	0	0	0		10
10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4		1	0	0	0	1		11
10	10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4		1	0	0	1	0		12
10	10	10	10	10	10	10	10	10	10	10	10	10	-4	-4		1	0	0	1	1		13
10	10	10	10	10	10	10	10	10	10	10	10	10	10	-4		1	0	1	0	0		14
10	10	10	10	10	10	10	10	10	10	10	10	10	10	10		1	0	1	0	1		15
Overflow

#### Boolean Expressions
To get the boolean expressions for each of the BCD outputs, I used previous Truth Table to find individual boolean expression that constrained an output to only be high during a certain range. I then combined these expressions into a set of five for each output using the OR operation, which are listed below:
E = U
D = S.bar U
C = O. bar R + Y
B = M.bar O + Q.bar S + W.bar Y
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Circuit Diagram
The circuit diagrams of each outputs are the result of them being converted into NAND gates and then undergoing simplification.
The exception to this is Output A, which also has three OR gates. The reason for this is that the three OR operations would be made up of nine NAND gates, which would require three quad chip IC’s. By using OR gates directly, it reduces the cost and complexity of the system, as only one quad chip IC will be required using three OR gates for the three OR operations. Furthermore, it also reduces the complexity of wiring within the Sub-System, due to their being less logic gates.
An alternative Sub-System using only NAND gates can be seen at Alternative Sub-Systems Priority Encoder Output A on page 17.
##### Output E

##### Output D

##### Output C

##### Output B

##### Output A

#### Test Diagram
##### Output E
##### Output D
##### Output C
##### Output B
##### Output A

#### Test Tables
Test №	Encoder In / ±1V					Expected Out / V
	L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		E	D	C	B	A
1	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	0
2	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	5
3	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	5	0
4	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	5	5
5	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	5	0	0
6	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	5	0	5
7	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	5	5	0
8	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4		0	0	5	5	5
9	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4		0	5	0	0	0
10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4		0	5	0	0	5
11	10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4		5	0	0	0	0
12	10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4		5	0	0	0	5
13	10	10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4		5	0	0	5	0
14	10	10	10	10	10	10	10	10	10	10	10	10	10	-4	-4		5	0	0	5	5
15	10	10	10	10	10	10	10	10	10	10	10	10	10	10	-4		5	0	5	0	0
16	10	10	10	10	10	10	10	10	10	10	10	10	10	10	10		5	0	5	0	5

Test №	Measured Out / V
	E	D	C	B	A
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16

#### Test Procedure
#### Test Review

### Seven Segment Display Sub-System
SN74184 Binary to BCD chip (https://www.alldatasheet.com/datasheet-pdf/view/98235/TI/SN74184.html).

CD74HCT4511E IC BCD to Seven Seg decoder.
https://www.ti.com/lit/ds/symlink/cd54hc4511.pdf
NAND WORKS WITH -5V ###### HOWEVER NEEDS -5V GROUND
#### Circuit Diagram
#### Test Diagram
The inputs to the seven seg don’t need to be measured, because whether the bulb lights up or not is valid for testing.
#### Test Table
#### Test Procedure
#### Test Review

## Alternative Sub-Systems
### Analogue In
### Priority Encoder Output A

### Priority Encoder Binary
This is the previous design of the Priority Encoder Sub-System (on page 10), where a binary signal was output rather than a BCD signal. More information can be found at the Priority Encoder Sub-System.
An interesting coincidence is that the boolean expression for output “A” is identical between both the BCD and binary design. Therefore, the circuit design for output “A” has not changed.
#### Truth Table
Encoder In/V					Binary Out / Logic
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		D	C	B	A
0	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	0
5	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	1
5	5	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	1	0
5	5	5	0	0	0	0	0	0	0	0	0	0	0	0		0	0	1	1
5	5	5	5	0	0	0	0	0	0	0	0	0	0	0		0	1	0	0
5	5	5	5	5	0	0	0	0	0	0	0	0	0	0		0	1	0	1
5	5	5	5	5	5	0	0	0	0	0	0	0	0	0		0	1	1	0
5	5	5	5	5	5	5	0	0	0	0	0	0	0	0		0	1	1	1
5	5	5	5	5	5	5	5	0	0	0	0	0	0	0		1	0	0	0
5	5	5	5	5	5	5	5	5	0	0	0	0	0	0		1	0	0	1
5	5	5	5	5	5	5	5	5	5	0	0	0	0	0		1	0	1	0
5	5	5	5	5	5	5	5	5	5	5	0	0	0	0		1	0	1	1
5	5	5	5	5	5	5	5	5	5	5	5	0	0	0		1	1	0	0
5	5	5	5	5	5	5	5	5	5	5	5	5	0	0		1	1	0	1
5	5	5	5	5	5	5	5	5	5	5	5	5	5	0		1	1	1	0
5	5	5	5	5	5	5	5	5	5	5	5	5	5	5		1	1	1	1
Overflow

#### Boolean Expressions
These are the boolean expressions that I derived for the binary outputs:
D = S
C = O. bar S + W
B = Y + U.bar W + Q.bar S + M.bar O
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Circuit Diagram
##### Output D
##### Output C
##### Output B
##### Output A
Not changed, see comment at Priority Encoder Binary on page 17.

## System Realisation

## Evaluation