## System Planning
Name:
ID:
### Problem
What, why, who, where.
Research of a specific example.
Alice is a mum to her 5 year old daughter (Jessie). Alice is helping Jessie to learn how to add numbers together at home to help her get ahead in primary school. However, Alice is often busy and cannot always supervise Jessie and check her work.
Jessie finds using calculators to be unintuitive and hard, as she finds it easier to understand analogue systems. My adder system will help Alice by allowing Jessie to check her if she added two numbers together correctly, especially as the inputs are both analogue, allowing Jessie to comprehend it easier.
### Specification
At least 4 qualitative and 4 quantitative system specifications (a list of 8).
Electronic parameters (e.g. time, frequency, current, voltage, power (inc. tolerances)
## System Development
Have at least 3 alternate sub-system/circuits
### Analogue Input Sub-System
#### Circuit Diagram

#### Test Diagram

#### Test Table
Each test only list the expected values for components relevant to the test.
Test Number	Switch Position	Expected Output	Measured Output
1	One: Closed	Analogue One: 0±0.1V / Pot One: 0±0.1V	Analogue One: 0.00±0.005V / Pot One: 0.00±0.005V
2	Two: Closed	Analogue Two: 0±0.1V / Pot Two: 0±0.1V	Analogue Two: 0.00±0.005V / Pot Two: 0.00±0.005V
3	One: Closed	Analogue One: -5±0.1V / Pot One: -5±0.1V	Analogue One: -4.96±0.005V / Pot One: -4.96±0.005V
4	Two: Closed	Analogue Two: -5±0.1V / Pot Two: -5±0.1V	Analogue Two: -4.99±0.005V / Pot Two: -4.99±0.005V
5	One: Open	Analogue One: 0±0.1V / Pot One: -5±0.1V	Analogue One: 0.00±0.005V / Pot One: -4.96±0.005V
6	Two: Open	Analogue Two: 0±0.1V / Pot Two: -5±0.1V	Analogue Two: 0.00±0.005V / Pot Two: -4.99±0.005V

#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust potentiometer one (VR2) / potentiometer two (VR1) until Pot One / Pot Two displays the value expected.
3) Measure and record the value of Analogue One and Pot One / Analogue Two and Pot Two.
4) Repeat from step 2 for all the tests.
#### Test Review
The testing of this sub-system went well, with no issues during testing and all tests producing outputs that are within the desired tolerance range. However, at the time of testing I had to substitute both push to break switches with push to make switches due there being no push to break switches available at the time of testing. This did not impact the execution of the test, as in the “switch position” column it states whether a switch is open or closed, which produces the same behaviour with both push to break and push to make switches.
The largest outlier was the minimum voltage output from Pot One, with it being +0.04V from the expected output in tests 3 and 5, however it was still within specification as the maximum allowed voltage within tests 3 and 5 is -4.90V.
### Mixer Sub-System
Had issues with original input of +5 0, changed to +5, -5 which fixed voltages close to 0. Had to change to +12, -5 to get correct voltages at 5+ volts.
#### Circuit Diagram

#### Test Diagram

#### Test Table
The expected outcome of the test is predicted using the equation: V_{out} = R_{f} ( {frac { V_{1} } {R_{1}}} + frac {V_{2}} {R_{2}} ) , where V_{ 1 } is analogue input one, V_{ 2 } is analogue input two, and R_{f} R_{ 1 } R_{ 2 } are at 1±0.025KΩ.
Test Number	Test Inputs	Expected Outcome	Measured Outcome
1	Analogue One: 0±0.04V / Analogue Two: 0±0.04V	Mixer Output: 0±0.04V	Mixer Output: 0.00±0.04V
2	Analogue One: -2±0.04V / Analogue Two: 0±0.04V	Mixer Output: 2±0.04V	Mixer Output: 2.01±0.04V
3	Analogue One: 0±0.04V / Analogue Two: -2±0.04V	Mixer Output: 2±0.04V	Mixer Output: 2.01±0.04V
4	Analogue One: -2±0.04V / Analogue Two: -2±0.04V	Mixer Output: 4±0.04V	Mixer Output: 4.01±0.04V
5	Analogue One: -4±0.04V / Analogue Two: -4±0.04V	Mixer Output: 8±0.04V	Mixer Output: 8.02±0.04V

#### Test procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust the potentiometer for Analogue One until the voltage measured from Analogue One In is at the required voltage for the test.
3) Adjust the potentiometer for Analogue Two until the voltage measured from Analogue Two In is at the required voltage for the test.
4) Measure & record the voltage from Mixer Output.
5) Repeat from step 2 for all the tests.
#### Test Review
Went well with no issues.
### Resistor Ladder Sub-System
#### Circuit Diagram
The purpose of R17 (8.2KΩ) is to cause the Overflow voltage to be at about 8V, because this is the highest voltage output tested for the Mixer Sub-System.
Ideally R17 would have a resistance of exactly 8KΩ, which would cause the output of Overflow to be exactly at 8V. However, closest E24 resistance to 8KΩ is 8.2KΩ, so I have to use an 8.2KΩ resistor for R17. This causes the Overflow voltage to be 7.93V, which is calculated by:
V_{ Overflow } = frac {R_{1..16} times V_{"in"}} {R_{1..16} + R_{17}} = frac {"16K" times 12} {"16K" times "8.2K"} = "7.93V"
The value of R17 being 8.2KΩ rather than 8KΩ does not effect the overall function of the system, so I have decided that the measured output values will be compared against the values predicted using the 8.2KΩ resistor.
#### Test Diagram

#### Test Table
Add test for measuring value of 8.2K resistor?
The Expected Output for each test is calculated using the formula V_{ out } = frac { R_{2} times V_{ "in" } } {R_{2} times {R_{1}}} where:
R_{ 2 } = The total resistance from the 12V in to the measured output.
R_{ 1 } = The total resistance from the 0V out to the measured output.
V_{ "in" } = 12V.
V_{ out } = The expected output voltage.
Test Number	Expected Output	Measured Output
1	Overflow: 7.93±	Overflow: ±
2	Z: 7.44±	Z: ±
3	Y: 6.94±	Y: ±
4	X: 6.45±	X: ±
5	W: 5.95±	W: ±
6	V: 5.45±	V: ±
7	U: 4.96±	U: ±
8	T: 4.46±	T: ±
9	S: 3.97±	S: ±
10	R: 3.47±	R: ±
11	Q: 2.98±	Q: ±
12	P: 2.48±	P: ±
13	O: 1.98±	O: ±
14	N: 1.49±	N: ±
15	M: 0.99±	M: ±
16	L: 0.50±	L: ±
17	R34: 8.2±0.205KΩ	R34: 8.09±0.005KΩ

#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Measure and record the required outputs for each test.
#### Test Review

### Comparator Chain Sub-System
Asked Sir what input voltages the NAND IC accept as input so I know what to output from the Op Amps. The chips are CMOS chips.
Measured the voltage ranges of chip on breadboard.
Input switches at 2.5V both ways – can use 5V & 0V for op amps
Op Amp IC used: Texas Instruments TL084CN Bi-FET Quad Operational Amplifier DIL14
#### Circuit Diagram

#### Test Diagram

#### Test Table
#### Test Procedure
#### Test Review

### Priority Encoder Sub-System
The Priority Encoder Sub-System originally output a binary signal, which was going to be converted into a BCD signal by the Seven Segment Display Sub-System before being converted into the seven segment display format. However, I was not able to acquire the required chip (SN74184), which would have done the conversion from binary to BCD, due to supply shortages. Because of this I had to redesign this sub-system to output a BCD signal, making the binary to BCD conversion redundant.
The original binary priority encoder can be seen at Alternative Sub-Systems Priority Encoder Binary on page 13.
#### Truth Table
Encoder In/V					BCD Out/Logic					10’s
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		E	D	C	B	A		##
0	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	0	0		0
5	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	0	1		1
5	5	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	1	0		2
5	5	5	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	1	1		3
5	5	5	5	0	0	0	0	0	0	0	0	0	0	0		0	0	1	0	0		4
5	5	5	5	5	0	0	0	0	0	0	0	0	0	0		0	0	1	0	1		5
5	5	5	5	5	5	0	0	0	0	0	0	0	0	0		0	0	1	1	0		6
5	5	5	5	5	5	5	0	0	0	0	0	0	0	0		0	0	1	1	1		7
5	5	5	5	5	5	5	5	0	0	0	0	0	0	0		0	1	0	0	0		8
5	5	5	5	5	5	5	5	5	0	0	0	0	0	0		0	1	0	0	1		9
5	5	5	5	5	5	5	5	5	5	0	0	0	0	0		1	0	0	0	0		10
5	5	5	5	5	5	5	5	5	5	5	0	0	0	0		1	0	0	0	1		11
5	5	5	5	5	5	5	5	5	5	5	5	0	0	0		1	0	0	1	0		12
5	5	5	5	5	5	5	5	5	5	5	5	5	0	0		1	0	0	1	1		13
5	5	5	5	5	5	5	5	5	5	5	5	5	5	0		1	0	1	0	0		14
5	5	5	5	5	5	5	5	5	5	5	5	5	5	5		1	0	1	0	1		15
Overflow

#### Boolean Expressions
I derived the boolean expressions for each of the BCD outputs, which are listed bellow.
E = U
D = S.bar U
C = O. bar R + Y
B = M.bar O + Q.bar S + W.bar Y
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Circuit Diagram
The circuit diagrams of each outputs are the result of them being converted into NAND gates and then undergoing simplification.
The exception to this is Output A, which also has three OR gates. The reason for this is that the three OR operations would be made up of nine NAND gates, which would require three quad chip IC’s. By using OR gates directly, it reduces the cost and complexity of the system, as only one quad chip IC will be required using three OR gates for the three OR operations. Furthermore, it also reduces the complexity of wiring within the Sub-System, due to their being less logic gates.
An alternative Sub-System using only NAND gates can be seen at Alternative Sub-Systems Priority Encoder Output A on page 13.
##### Output E

##### Output D

##### Output C

##### Output B

##### Output A

#### Test Diagram
#### Test Table
#### Test Procedure
#### Test Review

### Seven Segment Display Sub-System
SN74184 Binary to BCD chip (https://www.alldatasheet.com/datasheet-pdf/view/98235/TI/SN74184.html).
4511 IC BCD to Seven Seg decoder.
#### Circuit Diagram
#### Test Diagram
The inputs to the seven seg don’t need to be measured, because whether the bulb lights up or not is valid for testing.
#### Test Table
#### Test Procedure
#### Test Review

## Alternative Sub-Systems
### Analogue In
### Priority Encoder Output A

### Priority Encoder Binary
This is the previous design of the Priority Encoder Sub-System (on page 9), where a binary signal was output rather than a BCD signal. More information can be found at the Priority Encoder Sub-System.
An interesting coincidence is that the boolean expression for output “A” is identical between both the BCD and binary design. Therefore, the circuit design for output “A” has not changed.
#### Truth Table
Encoder In/V					Binary Out
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		D	C	B	A
0	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	0
5	0	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	0	1
5	5	0	0	0	0	0	0	0	0	0	0	0	0	0		0	0	1	0
5	5	5	0	0	0	0	0	0	0	0	0	0	0	0		0	0	1	1
5	5	5	5	0	0	0	0	0	0	0	0	0	0	0		0	1	0	0
5	5	5	5	5	0	0	0	0	0	0	0	0	0	0		0	1	0	1
5	5	5	5	5	5	0	0	0	0	0	0	0	0	0		0	1	1	0
5	5	5	5	5	5	5	0	0	0	0	0	0	0	0		0	1	1	1
5	5	5	5	5	5	5	5	0	0	0	0	0	0	0		1	0	0	0
5	5	5	5	5	5	5	5	5	0	0	0	0	0	0		1	0	0	1
5	5	5	5	5	5	5	5	5	5	0	0	0	0	0		1	0	1	0
5	5	5	5	5	5	5	5	5	5	5	0	0	0	0		1	0	1	1
5	5	5	5	5	5	5	5	5	5	5	5	0	0	0		1	1	0	0
5	5	5	5	5	5	5	5	5	5	5	5	5	0	0		1	1	0	1
5	5	5	5	5	5	5	5	5	5	5	5	5	5	0		1	1	1	0
5	5	5	5	5	5	5	5	5	5	5	5	5	5	5		1	1	1	1
Overflow

#### Boolean Expressions
These are the boolean expressions that I derived for the binary outputs:
D = S
C = O. bar S + W
B = Y + U.bar W + Q.bar S + M.bar O
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Circuit Diagram
##### Output D
##### Output C
##### Output B
##### Output A
Not changed, see comment at Priority Encoder Binary on page 13.

## System Realisation

## Evaluation