# Microcontroller fire alarm system
## Microcontroller pin layout
The pin layout of the PICAXE microcontroller is given by the following image. Any pin numbers used throughout this document are in reference to this diagram.

## Language used in this document
The following definitions apply to the vocabulary used within this document.
If one of the bellow terms is written in italics, then it is referring to the definitions bellow. However, if there is text that is not italic in which one of these definitions is used it is up to reader discretion whether if refers to the bellow definitions, though most of the time it will not.
#### High
In the context of referring to a voltage the term high is defined as 5V±1V.
#### Low
In the context of referring to a voltage the term low is defined as 0V±1V.
#### Override switch
In the context of referring to an input for the PICAXE microcontroller the term override switch is defined as pin 18 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term override switch is defined as PORT A bit 1.
#### Sensor one
In the context of referring to an input for the PICAXE microcontroller the term sensor one is defined as pin 17 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one is defined as PORT A bit 0.
#### Sensor two
In the context of referring to an input for the PICAXE microcontroller the term sensor two is defined as pin 16 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two is defined as PORT A bit 7.
#### Sensor three
In the context of referring to an input for the PICAXE microcontroller the term sensor three is defined as pin 15 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three is defined as PORT A bit 6.
#### Alarm
In the context of referring to an output for the PICAXE microcontroller the term alarm is defined as pin 6 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term alarm is defined as PORT B bit 0.
#### Sensor one indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor one indicator is defined as pin 7 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one indicator is defined as PORT B bit 1.
#### Sensor two indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor two indicator is defined as pin 8 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two indicator is defined as PORT B bit 2.
#### Sensor three indicator
In the context of referring to an output for the PICAXE microcontroller the term sensor three indicator is defined as pin 9 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three indicator is defined as PORT B bit 3.
#### Sensor one sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor one sprinkler is defined as pin 10 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor one sprinkler is defined as PORT B bit 4.
#### Sensor two sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor two sprinkler is defined as pin 11 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor two sprinkler is defined as PORT B bit 5.
#### Sensor three sprinkler
In the context of referring to an output for the PICAXE microcontroller the term sensor three sprinkler is defined as pin 12 on the PICAXE microcontroller.
In the context of parameters within the PICAXE microcontroller code the term sensor three sprinkler is defined as PORT B bit 6.
#### Triggered
In the context of referring to sensor one, sensor two, or sensor three the term triggered is defined as the mentioned sensor being high for 500±100ms. Furthermore, if the mentioned sensor continues to be high for over 500±100ms, then it will only count as a single instance of being triggered, regardless of how long the mentioned sensor is high for.
#### The Outputs
In the context of referring to output pins from the PICAXE microcontroller, the term the outputs is defined as alarm, sensor one indicator, sensor two indicator, sensor three indicator, sensor one sprinkler, sensor two sprinkler, & sensor three sprinkler.
## System Planning

### Problem
Muhammad owns a small office which he runs a business from. Muhammad’s office is in need of a fire alarm & sprinkler system, as the office needs to comply with fire safety regulations. Furthermore, Muhammad stores valuable prototypes of products at the office, which would be destroyed in the event of a fire. An alarm & sprinkler system will ensure the safety of these prototypes.
### Specification
1) While the override switch is high the outputs will be forced low.
2) When sensor one indicator is high, the sensor one sprinkler will be high.
3) When sensor two indicator is high, the sensor two sprinkler will be high.
4) When sensor three indicator is high, the sensor three sprinkler will be high.
5) When sensor one is triggered then the LED associated to sensor one indicator will be illuminated.
6) When sensor two is triggered then the LED associated to sensor two indicator will be illuminated.
7) When sensor three is triggered then the LED associated to sensor three indicator will be illuminated.
8) When sensor one is triggered the alarm will be high.
9) When sensor two is triggered the alarm will be high.
10) When sensor three is triggered the alarm will be high.
11) After the override switch has been released (set low), sensor one, sensor two, & sensor three can be triggered again.
12) Non-consecutive high on sensor one, sensor two, & sensor three will reset the time taken for the corresponding sensor to be triggered.
## System Development
### Flowchart
See attached resources for diagram.
1: This is the start of the program.
2: This checks if the override switch is high, if it is not then sensor one, sensors two, & sensor three will be checked. If it has then it will return back to the start after executing other relevant instructions without passing through the checks for sensor one, sensor two, & sensor three so they cannot be triggered.
3: Checks if sensor one has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
4: Checks if sensor two has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
5: Checks if sensor three has been triggered. The reason that it makes sure that the input is high for over 500±100ms is to make sure false positives from a singular voltage spike to high cannot cause erroneous responses.
6: This stops any ongoing alarms by setting the alarm to low.
7: This stops any ongoing sprinklers by setting sensor one sprinkler, sensor two sprinkler, & sensor three sprinkler to low.
8: This turns off any illuminated indicator LEDS by setting sensor one indicator, sensor two indicator, & sensor three indicator to low.
9: This turns on the sensor one sprinkler by setting it to high.
10: This turns on the alarm by setting it to high.
11: This turns on the sensor two sprinkler by setting it to high.
12: This turns on the sensor three sprinkler by setting it to high.
13: This turns on the sensor one indicator by setting it to high.
14: This turns on the sensor two indicator by setting it to high.
15: This turns on the sensor three indicator by setting it to high.
### Code Description
At simplistic level the code can be thought of as checking if sensor one, sensor two, or sensor three has been triggered. And setting the appropriate outputs (sensor one indicator & sensor one sprinkler/sensor two indicator & sensor two sprinkler/sensor three indicator & sensor three sprinkler) & alarm to high. Unless the override switch has been pressed, which forces the outputs to low.

Before describing the code structure, there are a few variables, which are defined in the “vars” label used throughout the code that will be explained.
The “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count” all keep track of the number of consecutive cycles that sensor one, sensor two, & sensor three, have been triggered respectively.
The “Result” variable is used to temporarily store the result of calculations when the working register is overwritten by other operations before the calculation result is needed.

At a deeper level, the code executed by the PICAXE microcontroller performs what will be referred to as a cycle every 100±20ms. Before the first cycle, basic initialisation & variable definitions are executed. After that, cycles are continuously executed until the PICAXE microcontroller stops receiving input power (on pin 14).
A cycle consists of multiple stages:
1) Checking if the override switch is high.
2) Checking if sensor one is high.
3) Checking if sensor two is high.
4) Checking if sensor three is high.
5) Handling non-consecutive increments of “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count”
6) Waiting for 100ms.
7) Going back to step 1.

Each stage will be expanded upon bellow.
#### Stage One
In stage one the code checks whether the override switch switch is high. If the override switch is high, then the code sets all of PORTB to low & resets “Sprinkler_One_Count”, “Sprinkler_Two_Count”, & “Sprinkler_Three_Count” to 0. This will stop any alarms, indicators, & sprinklers that might be connected to the outputs, which is where the “override switch” gets its name from. It overrides any other outputs.
Furthermore, after doing this it directly goes to the start of the cycle again, skipping any checks for sensor one, sensor two, & sensor three. This ensures that the outputs must remain low when the override switch is high.
#### Stage Two
In stage two the code checks whether sensor one is high. If it is low, then the subroutine exits early and the code moves onto stage three. If it is high then it checks if “Sprinkler_One_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor one indicator, & sensor one sprinkler are set high. If it has a value less then five, the “Sprinkler_One_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_One_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Three
In stage three the code checks whether sensor two is high. If it is low, then the subroutine exits early and the code moves onto stage four. If it is high then it checks if “Sprinkler_Two_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor two indicator, & sensor three sprinkler are set high. If it has a value less then five, the “Sprinkler_Two_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_Two_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Four
In stage four the code checks whether sensor three is high. If it is low, then the subroutine exits early and the code moves onto stage five. If it is high then it checks if “Sprinkler_Three_Count” has a value of five (by performing bit checks on the register). If it has a value of five then the alarm, sensor three indicator, & sensor three sprinkler are set high. If it has a value less then five, the “Sprinkler_Three_Count” is incremented (increased by one).
The “Result” register is used during this to store whether the “Sprinkler_Three_Count” register has a value of five, as the working register would be overwritten & checking for a value of 5 takes a lot of instruction cycles.
#### Stage Five
Using bit checks on sensor one, sensor two, & sensor three the PICAXE microcontroller checks if any of them are high or low. If the input is low then the associated sprinkler count is set to 0. This prevents occasional voltage spikes on sensor one, sensor two, and/or sensor three from eventually incrementing the associated sprinkler count to 5. However, if the input is high, then no action is taken. This only allows the associated sprinkler count for a sensor to reach 5 if the sensor has been measured as high for 500±100ms (five cycles).
#### Stage Six
The PICAXE microcontroller then sleeps for 100±20ms, by calling the subroutine “wait100ms”. This allows for the time cycle will take to be known & therefore how long it will take for sensor one, sensor two, and/or sensor three to be triggered.
#### Stage Seven
The code goes back to stage one & continues to repeat cycles indefinitely.

### Code
See attached resources for full code.

### Commands Used
1: “clrf”
2: “bsf”
3: “movlw”
4: “movwf”
5: “bcf”
6: “equ”
7: “btfsc”
8: “goto”
9: “call”
10: “btfss”
11: “incf”
12: “return”
### Assembling
#### Problem One: Variable naming
When defining the registers that are used to store how many times each sensors has been set, I mistakenly used the same name for each register.
I fixed this by changing each name to unique ones.

#### Problem two: Forgetting comma
When I was working on the override switch functionality, I accidentally typed “btfsc PORTA 0” instead of “btfsc PORTA, 0”. This resulted in the following syntax error.
I easily fixed this by changing it to “btfsc PORTA, 0”

#### Problem three: Working register issues
During implementing the sensor one subroutine, I was attempting to store the result of a calculation into the W register, & I got a syntax error when trying to do that with this instruction.

I wasn’t entirely sure why there was an issue with performing btfs* operations on the W register, other than for the reason that it is the working register. To circumnavigate this problem I created another registered to move the value into before checking it.

This allowed the program to compile without an issue.
#### Problem four: Typo
I made a typo when refering to the “Sprinkler_One_Count” register whilst rewritting my sprinkler subroutine. I easily fixed this by correcting the typo.
#### Problem five: Stack underflow
I made a mistake of calling a subroutine with “goto” instead of “call”, which resulted in a “Stack Underflow” error when I was testing it.
I easily fixed this by changing the “goto” to a “call” instruction.
#### Problem six: Wrong port bits
At the start of development I was using PORT A bits 0, 1, 2, & 3 for inputs. However, later on I released that bits 2 & 3 on PORT A were used to program the PICAXE chip. I decided that I didn’t want to have to keep changing the wiring of my circuit in between programming so I wired the circuit to use pin 18, 17, 16, 15 (PORTA bits 0, 1, 6, 7). However, I forgot to change this within my code.
I easily fixed this my modifying the bit tests to check the correct bits.

## System Realisation

### Circuit Diagram
This is the configuration of the circuit that will be used by customers when they install the system. It is also know as the “Deployed Configuration”.

### Components List
- 1x PICAXE microcontroller
- 4x Push to make switches
- 7x LED
- 7x 330Ω resistors
- 4x 10kΩ resistors
- 3x 100kΩ resistors
- 1x 10nF capacitor

### Photo Of Circuit
See attached resources for circuit photo.

### Evidence of Downloaded Program
#### Downloading Data

#### Downloading Program

#### Successfully Installed

### Test Equipment Circuit Diagram
This is the configuration of the circuit I will use to test that the entire system is functioning within the specification.
### Testing Circuit Evidence
See attached resources for testing evidence.
### Testing
Override switch, sensor one, sensor two, sensor three, are to be assumed low unless explicitly stated otherwise.
Between each test the override switch should be pressed for at least 500±100ms.
Input voltage of 5.00±0.005V
Specification	Test	Why	Expected Result	Actual Result
2, 5, 8	1: / Have sensor one high for over 500ms	To test if sensor one works as expected.	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – 4.35V / Sensor one indicator – 4.21V / Sensor one sprinkler – 4.32V
3, 6, 9	2: / Have sensor two high for over 500ms	To test if sensor two works as expected.	The following outputs will be high: alarm, sensor two indicator, sensor two sprinkler	Alarm – 4.23V / Sensor two indicator – 4.35V / Sensor two sprinkler – 4.05V
4, 7, 10	3: / Have sensor three high for over 500ms	To test if sensor three works as expected.	The following outputs will be high: alarm, sensor three indicator, sensor three sprinkler	Alarm – 4.26V / Sensor three indicator – 4.12V / Sensor three sprinkler – 4.39V
12	4: / Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms	To test that the sensor won’t trigger due to non-consecutive inputs.	All of the outputs will be low.	Alarm – 0.03V / Sensor one indicator – 0.03V / Sensor two indicator – 0.03V / Sensor three indicator – 0.02V / Sensor one sprinkler – 0.03V / Sensor two sprinkler – 0.03V / Sensor three sprinkler – 0.02V
2, 3, 4, 5, 6, 7, 8, 9, 10	5: / Have sensor one, sensor two, & sensor three high for over 500ms	If all of the corresponding sensor outputs will be triggered along with the alarm	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler, sensor two indicator, sensor two sprinkler, / sensor three indicator, sensor three sprinkler	Alarm – 4.20V / Sensor one indicator – 4.18V / Sensor two indicator – 4.28V / Sensor three indicator – 3.68V / Sensor one sprinkler – 4.35V / Sensor two sprinkler – 4.22V / Sensor three sprinkler – 4.41V
1	6: / Have sensor one high for 1000ms & the override switch high for the duration of the test	If the override switch stops the sensors from triggering	All of the outputs will be low.	Alarm – 0.03V / Sensor one indicator – 0.02V / Sensor two indicator – 0.03V / Sensor three indicator – 0.02V / Sensor one sprinkler – 0.03V / Sensor two sprinkler – 0.03V / Sensor three sprinkler – 0.03V
11	7: / Have the override switch & sensor one high initially. When the test starts set override switch low. Then keep sensor one high for 1000ms	If the sensors can re-trigger after they have been overridden	500±100ms after the override switch has been released the following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – 4.09V / Sensor one indicator – 4.19V / Sensor one sprinkler – 4.31V

### Analysis Of Test Results
Overall the actual results I obtained from my test match up to the specification I outlined within my expected results. However, there was an outlier in test 5, with the sensor three indicator voltage, which was at 3.68V.
Furthermore, during testing the time taken for sensor one, sensor two, & sensor three to be triggered was closer to 750±150ms rather than the expected 500±100ms. However, this did not effect the results of the test, as with tests 1, 2, 3, & 5, they specify a minimum time, so the increase time taken to trigger does not effect the outcome. The test 4 specifies a time shorter than both the predicted & observed time period, so the increased time period did not effect the results. The tests 6 & both specify time periods that are over the observed time period, so the increased time taken to trigger does not effect the result of the tests.
Aside from this, the system worked consistently & reliably throughout the duration of testing. With all measured results being reproducible.
Test	Expected Result	Actual Result	Analysis
1: / Have sensor one high for over 500ms	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – 4.35V / Sensor one indicator – 4.21V / Sensor one sprinkler – 4.32V	PASS / All measured outputs were within the outlined tolerance.
2: / Have sensor two high for over 500ms	The following outputs will be high: alarm, sensor two indicator, sensor two sprinkler	Alarm – 4.23V / Sensor two indicator – 4.35V / Sensor two sprinkler – 4.05V	PASS / All measured outputs were within the outlined tolerance.
3: / Have sensor three high for over 500ms	The following outputs will be high: alarm, sensor three indicator, sensor three sprinkler	Alarm – 4.26V / Sensor three indicator – 4.12V / Sensor three sprinkler – 4.39V	PASS / All measured outputs were within the outlined tolerance.
4: / Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms / Have sensor one low for at least 100ms / Have sensor one high for 300±100ms	All of the outputs will be low.	Alarm – 0.03V / Sensor one indicator – 0.03V / Sensor two indicator – 0.03V / Sensor three indicator – 0.02V / Sensor one sprinkler – 0.03V / Sensor two sprinkler – 0.03V / Sensor three sprinkler – 0.02V	PASS / All measured outputs were within the outlined tolerance.
5: / Have sensor one, sensor two, & sensor three high for over 500ms	The following outputs will be high: alarm, sensor one indicator, sensor one sprinkler, sensor two indicator, sensor two sprinkler, / sensor three indicator, sensor three sprinkler	Alarm – 4.20V / Sensor one indicator – 4.18V / Sensor two indicator – 4.28V / Sensor three indicator – 3.68V / Sensor one sprinkler – 4.35V / Sensor two sprinkler – 4.22V / Sensor three sprinkler – 4.41V	FAIL / Alarm, Sensor one indicator, Sensor two indicator, Sensor one sprinkler, Sensor two sprinkler, & Sensor three sprinkler were measured within tolerance. / Sensor three indicator was measured outside of the outlined voltage tolerance. However, the LED indicator attached to this output did illuminate, so my tolerance limits are overly strict.
6: / Have sensor one high for 1000ms & the override switch high for the duration of the test	All of the outputs will be low.	Alarm – 0.03V / Sensor one indicator – 0.02V / Sensor two indicator – 0.03V / Sensor three indicator – 0.02V / Sensor one sprinkler – 0.03V / Sensor two sprinkler – 0.03V / Sensor three sprinkler – 0.03V	PASS / All measured outputs were within the outlined tolerance.
7: / Have the override switch & sensor one high initially. When the test starts set override switch low. Then keep sensor one high for 1000ms	500±100ms after the override switch has been released the following outputs will be high: alarm, sensor one indicator, sensor one sprinkler	Alarm – 4.09V / Sensor one indicator – 4.19V / Sensor one sprinkler – 4.31V	PASS / All measured outputs were within the outlined tolerance.

## Evaluation

### Progress & Performance
Reflect upon the progress & performance
I have made lots of progress, especially in regards to PICAXE assembly. This is because the majority of my solutions complexity lies within the code programmed onto the microcontroller. Additionally, I’m a strong believer in learning by doing, with this project providing me a more than ample opportunity to get acquainted with the inner workings of the PICAXE microcontroller.
Overall I would evaluate the performance of my produced system is adequate. One area of concern would be the difference between the predicted timing & the observed timing during testing. However, I do no think that this difference effects the core performance of the system, as the required functionality (sounding an alarm & enabling sprinklers) is still achieved, if only a faction of second later than planned for.
Other than the timing, the produced system meets all of the predicted specifications outlined within the testing criteria, other than an anomaly in test 5.
### Improvements
Specify implementation.
#### Improvement One
The first improvement that I would make to my system is to require the override switch to be high for 500±100ms before it the input would be acted upon. This will improve the resilience of the system against potential voltage spikes on the override switch, this would be a major issue if a voltage spike occurs during a fire as it will force the alarm, sensor one/two/three indicator, sensor one/two/three sprinkler outputs to low.
#### Improvement Two
The second improvement is combining the sensor one indicator & sensor one sprinkler into one output, combining sensor two indicator & sensor two sprinkler into one output, and combining sensor three indicator & sensor three sprinkler into one output. As they only ever set high or low in the listed pairs. They are separated due to functionality in prototype code that originally required this.
Combining these outputs together would reduce wiring complexity of the physical circuit & eliminate the possibility of the two outputs getting out of sync with each other.