# Analogue Adder
ADD REFERENCES
REWRITE TESTING PROCEDURE
UPDATE PRIORITY ENCODER D OUTPUT
SPECIFICATION NEEDS TO REFLECT TESTS?
## System Planning
Name:
ID:
### Problem
Alice is a mum to her 5 year old daughter (Jessie). Alice is helping Jessie to learn how to add numbers together at home to help her get ahead in primary school. However, Alice is often busy and cannot always supervise Jessie and check her work. My adder system will help Alice by allowing Jessie to check her if she added two numbers together correctly, without Alice having to come and check her work constantly.
Other calculators available, such as the “aristotle-calculator” (https://www.ukprinting.com/aristotle-calculator), have multiple buttons that with advanced features such as adding and subtracting values from the calculator memory. These extra buttons can cause an issue when they are accidentally pressed, which will confuse Jessie. Compounding these issues, the calculator allows for inputs of multiple digits potentially causing Jessie to feel overwhelmed, as she is only just learning to work with small numbers.
Additionally, scientific calculators such as the “FX-85GTCW” calculator (https://www.amazon.co.uk/Casio-FX-85GTCW-Black-Scientific-Calculator/dp/B0BVW38KQH?ref_=ast_sto_dp&th=1&psc=1) has even more advanced features that Jessie will not need to use until secondary school, or college. Combined with the plethora of labelled buttons, and multiple calculation modes, that most people do not learn to use until they are much older.
My adder does not have these issues, as it can only add small numbers together, making it more appropriate for a first introduction to addition.
### Specification
1) The sum of the two analogue inputs will be displayed by the seven segment display.
2) The user will have the option to see the value of analogue each input separately.
3) The numbers from and including 0 to 15 can be displayed as output.
4) The number displayed will change when one of the input potentiometers is turned sufficiently.
5) The voltage range for each analogue input will be between -5.0±0.1V and 0.0±0.1V.
6) The priority encoder will output 0.50±0.50V when an output is at logic level low.
7) The priority encoder will output 5.00±3.00V when an output is at logic level high.
8) The resolution (calculated with Resolution = frac { V_{range} } { 2^{bits} } ) of the ADC will be 0.496±0.05V at an input voltage of 12±0.0V.
## System Development
### Analogue Input Sub-System
This Sub-System is responsible for converting user input into an analogue voltage between -5±0.1V and 0±0.1V using potentiometers. The reason for this voltage range is that the Mixer Sub-System (on page 3) will invert the input voltage. Since the initial voltage is negative, the voltage output will be positive.
Additionally, push-to-break switches are placed between each potentiometer, allowing for the user to disable either input to see the value of the other input. Push-to-break switches are used instead of push-to-make, because I want the default behaviour to be showing the sum of the values. Furthermore, the user would have to hold down both buttons to see the desired output, which is not a good user experience.
#### Circuit Diagram

#### Test Diagram

#### Test Table
Each test only list the expected values for components relevant to the test.
Test Number	Switch Position	Expected Output / V	Measured Output / V
1	One: Closed	Analogue One: 0±0.1 / Pot One: 0±0.1	Analogue One: 0.00±0.005 / Pot One: 0.00±0.005
2	Two: Closed	Analogue Two: 0±0.1 / Pot Two: 0±0.1	Analogue Two: 0.00±0.005 / Pot Two: 0.00±0.005
3	One: Closed	Analogue One: -5±0.1 / Pot One: -5±0.1	Analogue One: -4.96±0.005 / Pot One: -4.96±0.005
4	Two: Closed	Analogue Two: -5±0.1 / Pot Two: -5±0.1	Analogue Two: -4.99±0.005 / Pot Two: -4.99±0.005
5	One: Open	Analogue One: 0±0.1 / Pot One: -5±0.1	Analogue One: 0.00±0.005 / Pot One: -4.96±0.005
6	Two: Open	Analogue Two: 0±0.1 / Pot Two: -5±0.1	Analogue Two: 0.00±0.005 / Pot Two: -4.99±0.005

#### Test Equipment
- Power supply.
- Voltmeter x 4 (or relocate one voltmeter).
- Screwdriver to adjust potentiometers.
#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust potentiometer one (VR2) / potentiometer two (VR1) until Pot One / Pot Two displays the value expected.
3) Measure and record the value of Analogue One and Pot One / Analogue Two and Pot Two.
4) Repeat from step 2 for all the tests.
#### Test Review
The testing of this sub-system went well, with no issues during testing and all tests producing outputs that are within the desired tolerance range (shown in the Test Table). However, at the time of testing I had to substitute both push to break switches with push to make switches due there being no push to break switches available at the time of testing. This did not impact the execution of the test, as in the “switch position” column it states whether a switch is open or closed, which produces the same behaviour with both push to break and push to make switches.
The largest absolute variance was the minimum voltage output from Pot One, with it being +0.04V (0.80%) from the expected output in tests 3 and 5, however it was still within specification as the maximum allowed voltage within tests 3 and 5 is -4.90V.
### Mixer Sub-System
The mixer (also known as a summing amplifier) is responsible for combining the two analogue inputs into a single analogue voltage.
The mixer has a gain of -1 (calculated with G = frac {-R_f} {R_"in"} = frac { -1KΩ } { 1KΩ } = -1 ) for both inputs, because I do not want to amplify the two inputs, only combine them together.
In the original design of this sub-system, I was using 5V and 0V for the positive and negative supply of the operational amplifier respectively. However, I was unsure if these values would allow the mixer to output a suitable voltage range, as the operational amplifier could possibly saturate before reaching either value. After testing the positive and negative saturation of the operational amplifier using 5V and 0V, it had a range much smaller than initially expected. I solved the issue by changing the supply voltages to 12V and -5V, which solved this issue, allowing for a much larger voltage range.
#### Circuit Diagram

#### Test Diagram

#### Test Table
The expected outcome of the test is predicted using the equation: V_{out} = R_{f} ( {frac { V_{1} } {R_{1}}} + frac {V_{2}} {R_{2}} ) , where V_{ 1 } is analogue input one, V_{ 2 } is analogue input two, and R_{f} R_{ 1 } R_{ 2 } are at 1±0.025KΩ.
Test Number	Test Inputs / V	Expected Outcome / V	Measured Outcome / V
1	Analogue One: 0±0.04 / Analogue Two: 0±0.04	Mixer Output: 0±0.04	Mixer Output: 0.00±0.005
2	Analogue One: -2±0.04 / Analogue Two: 0±0.04	Mixer Output: 2±0.04	Mixer Output: 2.01±0.005
3	Analogue One: 0±0.04 / Analogue Two: -2±0.04	Mixer Output: 2±0.04	Mixer Output: 2.01±0.005
4	Analogue One: -2±0.04 / Analogue Two: -2±0.04	Mixer Output: 4±0.04	Mixer Output: 4.01±0.005
5	Analogue One: -4±0.04 / Analogue Two: -4±0.04	Mixer Output: 8±0.04	Mixer Output: 8.02±0.005

#### Test Equipment
- Power supply.
- Voltmeter x 3 (or relocate one voltmeter).
- Screwdriver to adjust potentiometers.
#### Test procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Adjust the potentiometer for Analogue One until the voltage measured from Analogue One In is at the required voltage for the test.
3) Adjust the potentiometer for Analogue Two until the voltage measured from Analogue Two In is at the required voltage for the test.
4) Measure & record the voltage from Mixer Output.
5) Repeat from step 2 for all the tests.
#### Test Review
The test went well with no issues, with all measured outcomes being within the tolerance range of the expected outcome. Test 5 had the largest absolute variance, being 0.02V (0.25%) away from the exact expected outcome. However, this is still well within range.
### Resistor Ladder Sub-System
#### Circuit Diagram
The purpose of R17 (8.2KΩ) is to cause the Overflow voltage to be at about 8V, because this is the highest voltage output tested for the Mixer Sub-System.
Ideally R17 would have a resistance of exactly 8KΩ, which would cause the output of Overflow to be exactly at 8V. However, closest E24 resistance to 8KΩ is 8.2KΩ, so I have to use an 8.2KΩ resistor for R17. This causes the Overflow voltage to be 7.93V, which is calculated by:
V_{ Overflow } = frac {R_{1..16} times V_{"in"}} {R_{1..16} + R_{17}} = frac {"16K" times 12} {"16K" times "8.2K"} = "7.93V"
The value of R17 being 8.2KΩ rather than 8KΩ does not effect the overall function of the system, so I have decided that the measured output values will be compared against the values predicted using the 8.2KΩ resistor.
#### Test Diagram

#### Test Table
The Expected Output for each test is calculated using the formula V_{ out } = frac { R_{2} times V_{ "in" } } {R_{2} times {R_{1}}} where:
R_{ 2 } = The total resistance from the 12V in to the measured output.
R_{ 1 } = The total resistance from the 0V out to the measured output.
V_{ "in" } = 12V.
V_{ out } = The expected output voltage.
Test Number	Expected Output	Measured Output
1	Overflow: 7.93±0.05V	Overflow: 7.95
2	Z: 7.44±0.05V	Z: 7.44
3	Y: 6.94±0.05V	Y: 6.94
4	X: 6.45±0.05V	X: 6.44
5	W: 5.95±0.05V	W: 5.95
6	V: 5.45±0.05V	V: 5.45
7	U: 4.96±0.05V	U: 4.96
8	T: 4.46±0.05V	T: 4.46
9	S: 3.97±0.05V	S: 3.97
10	R: 3.47±0.05V	R: 3.46
11	Q: 2.98±0.05V	Q: 2.97
12	P: 2.48±0.05V	P: 2.48
13	O: 1.98±0.05V	O: 1.98
14	N: 1.49±0.05V	N: 1.49
15	M: 0.99±0.05V	M: 0.99
16	L: 0.50±0.05V	L: 0.49
17	R34: 8.2±0.205KΩ	R34: 8.09±0.005KΩ

#### Test Equipment
- Power supply.
- Voltmeter x 16 (or relocate one voltmeter).
- Ohmmeter
#### Test Procedure
1) Ensure that the circuit is created as shown in the test diagram.
2) Measure and record the required outputs for each test.
#### Test Review
The test very went with no issues, with all tests passing. The largest absolute variants is from test 1, where the measured value is 0.02V (0.25%) larger than the expected value. All other tests have either a 0.01V variants or are exactly as expected.
### Comparator Chain Sub-System
Originally, each operational amplifier had a V+ of 5V and a V- of 0V, however, this supply voltage range was too small for the operational amplifiers to function correctly, with voltage inputs from 1V to 0V and voltages above 5V producing unreliable results. I solved this by changing the V+ to 12V and V- to -5V, this allowed the operational amplifiers to produce correct results within the 0V to 8V range output by the Resistor Ladder Sub-System.
#### Circuit Diagram

#### Test Diagram

#### Test Table
The expected voltage range is calculated from the Resistor Ladder Sub-System on page 6. However, the expected results had to be adjusted, as the 12V output from my power supply gave an output of 12.10V. This disproportionally effected the tests 12 to 17 if this was not taken into account.
Test Number	Comparator Outputs / V	Expected V_{ ref } Range / V	Measured V_{ ref } Range / V
1	All: -4±1	0.00 to 0.50 (±0.05)	0.00 to 0.50
2	L: 10±1	0.50 to 1.00 (±0.05)	0.51 to 0.97
3	L, M: 10±1	1.00 to 1.50 (±0.05)	0.98 to 1.49
4	L to N: 10±1	1.50 to 2.00 (±0.05)	1.49 to 2.03
5	L to O: 10±1	2.00 to 2.50 (±0.05)	2.04 to 2.52
6	L to P: 10±1	2.50 to 3.00 (±0.05)	2.53 to 3.01
7	L to Q: 10±1	3.00 to 3.50 (±0.05)	3.02 to 3.50
8	L to R: 10±1	3.50 to 4.00 (±0.05)	3.51 to 4.00
9	L to S: 10±1	4.00 to 4.50 (±0.05)	4.01 to 4.49
10	L to T: 10±1	4.50 to 5.00 (±0.05)	4.50 to 4.99
11	L to U: 10±1	5.00 to 5.50 (±0.05)	5.00 to 5.48
12	L to V: 10±1	5.50 to 6.00 (±0.05)	5.49 to 6.04
13	L to W: 10±1	6.00 to 6.50 (±0.05)	6.05 to 6.54
14	L to X: 10±1	6.50 to 7.00 (±0.05)	6.55 to 7.05
15	L to Y: 10±1	7.00 to 7.50 (±0.05)	7.05 to 7.55
16	L to Z: 10±1	7.50 to 8.00 (±0.05)	7.55 to 8.04
17	L to Overflow: 10±1	8.00 to 9.00 (±0.05)	8.05 to 9.00

#### Test Equipment
- Power supply.
- Voltmeter x 16 (or relocate one voltmeter).
- Resistor chain to give the inputs “Overflow, Z, Y, X, W, V, U, T, S, R, Q, P, O, N, M, and L”.
- 10kΩ potentiometer.
#### Test Procedure
1) Set up the circuit as shown in the test diagram.
2) Ensure that the inputs “Overflow, Z, Y, X, W, V, U, T, S, R, Q, P, O, N, M, and L” are set at the corresponding voltage from the Resistor Ladder Sub-System Test Table on page 7, and that they maintain this voltage throughout the test.
3) Any outputs not mentioned in “Comparator Outputs” for a test are expected to have an output of -4±1V for the corresponding test.
4) The V_{ ref } can be adjusted by using VR1.
5) For each test, measure and record the lowest V_{ ref } that produces the same output from the operational amplifiers as listed in “Comparator Outputs”. Then measure and record the highest V_{ ref } that produces the same output. Combining both these measurements into a range where the operational amplifiers output the desired values.
V_{ ref } must not be adjust beyond the range 0V to 9V.
6) Repeat step five for every test.
#### Test Review
All the tests went well, with the measured range aligning with the expected range within the tolerances.
Tests 14 and 15 came the closest to failing, with the measured voltage range being at the maximum tolerance for the expected voltage range (±0.05V). With the 14 having a percentage variation of 0.83% and 0.77% for the low and high boundaries of the range respectively, and 15 having a variation of 0.71% and 0.67% for he low and high boundaries of the range respectively.
A large contributor to this deviance can be assigned to the ±5% tolerance of each resistor within the Resistor Ladder Sub-System, that was used to obtain the inverting operational amplifier inputs.
#### Interface issues
When I connected the Mixer output, all the comparitor outputs were at 4±1V, even when the Vref signal was at 0V.
When Vref was under 1.5V, all op amp high
When Vref above 1.5V op amps worked, but switched when X Y Z Ov switched on at Vref > ~5.25V

### Priority Encoder Sub-System
The Priority Encoder Sub-System converts the output from the Comparator Chain Sub-System (page 8) into a Binary Coded Decimal (BCD) signal.
#### Truth Table
Encoder In / ±1V					BCD Out / Logic					10’s
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		E	D	C	B	A
-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	0		0
10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	0	1		1
10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	1	0		2
10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	0	1	1		3
10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	0	0		4
10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	0	1		10
10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	1	0		6
10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4	-4		0	0	1	1	1		7
10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4	-4		0	1	0	0	0		8
10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4	-4		0	1	0	0	1		9
10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4	-4		1	0	0	0	0		10
10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4	-4		1	0	0	0	1		11
10	10	10	10	10	10	10	10	10	10	10	10	-4	-4	-4		1	0	0	1	0		12
10	10	10	10	10	10	10	10	10	10	10	10	10	-4	-4		1	0	0	1	1		13
10	10	10	10	10	10	10	10	10	10	10	10	10	10	-4		1	0	1	0	0		14
10	10	10	10	10	10	10	10	10	10	10	10	10	10	10		1	0	1	0	1		15
Overflow

#### Boolean Expressions
To get the boolean expressions for each of the BCD outputs, I used previous Truth Table to find individual boolean expression that constrained an output to only be high during a certain range. I then combined these expressions into a set of five for each output using the OR operation, which are listed below:
E = U
D = S.bar U
C = O. bar R + Y
B = M.bar O + Q.bar S + W.bar Y
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Circuit Diagram
The circuit diagrams of each outputs are the result of them being converted into NAND gates and then undergoing simplification.
The exception to this is Output A, which also has three OR gates. The reason for this is that the three OR operations would be made up of nine NAND gates, which would require three quad chip IC’s. By using OR gates directly, it reduces the cost and complexity of the system, as only one quad chip IC will be required using three OR gates for the three OR operations. Furthermore, it also reduces the complexity of wiring within the Sub-System, due to their being less logic gates.
An alternative Sub-System using only NAND gates can be seen at Alternative Sub-Systems Priority Encoder Output A on page 19.
##### Output E

##### Output D

##### Output C

##### Output B

##### Output A
#### Test Diagram
##### Output E
##### Output D
##### Output C
##### Output B
##### Output A

#### Test Tables
Test №	Encoder In / ±1V					Expected Out / V
	L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		E	D	C	B	A
1	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	0	0
2	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	0	5
3	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	5	0
4	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	5	5
5	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	0	0
6	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	0	5
7	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	5	0
8	12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	5	5
9	12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5		0	5	0	0	0
10	12	12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5		0	5	0	0	5
11	12	12	12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5		5	0	0	0	0
12	12	12	12	12	12	12	12	12	12	12	12	-5	-5	-5	-5		5	0	0	0	5
13	12	12	12	12	12	12	12	12	12	12	12	12	-5	-5	-5		5	0	0	5	0
14	12	12	12	12	12	12	12	12	12	12	12	12	12	-5	-5		5	0	0	5	5
15	12	12	12	12	12	12	12	12	12	12	12	12	12	12	-5		5	0	5	0	0
16	12	12	12	12	12	12	12	12	12	12	12	12	12	12	12		5	0	5	0	5

Test №	Measured Out / V
	E	D	C	B	A
1					0
2					5
3					0
4					5
5					0
6					5
7					0
8					5
9					0
10					5
11
12
13
14
15
16

Expected V_{ ref } Range / V	Expected Out / V					Measured Vref
	E	D	C	B	A
0.00 to 0.50 (±0.05)	0	0	0	0	0	0.00 – 0.42
0.50 to 1.00 (±0.05)	0	0	0	0	5	0.43 – 0.86
1.00 to 1.50 (±0.05)	0	0	0	5	0	0.87 – 1.35
1.50 to 2.00 (±0.05)	0	0	0	5	5	1.36 – 1.85
2.00 to 2.50 (±0.05)	0	0	5	0	0	1.86 – 2.30
2.50 to 3.00 (±0.05)	0	0	5	0	5	2.31 – 2.85
3.00 to 3.50 (±0.05)	0	0	5	5	0	2.86 – 3.29
3.50 to 4.00 (±0.05)	0	0	5	5	5	3.30 – 3.82
4.00 to 4.50 (±0.05)	0	5	0	0	0	3.83 – 4.36
4.50 to 5.00 (±0.05)	0	5	0	0	5	4.37 – 4.94
5.00 to 5.50 (±0.05)	5	0	0	0	0	4.95 – 5.69
5.50 to 6.00 (±0.05)	5	0	0	0	5	5.70 – 6.28
6.00 to 6.50 (±0.05)	5	0	0	5	0	6.29 – 6.68
6.50 to 7.00 (±0.05)	5	0	0	5	5	6.69 – 7.13
7.00 to 7.50 (±0.05)	5	0	5	0	0	7.14 – 7.54
	5	0	5	0	5	7.44 – 9.00

Test Number	Expected Behaviour	Observed Behaviour
20?	The priority encoder will produce the correct BCD output for the numbers 0 to 15 in the correct order as V_ref increases.	The priority encoder output the correct BCD numbers in the correct sequence as the V_ref increased.

#### Test Equipment
Rewrite for using comparitor out
- Power supply.
- Voltmeter x 5 (or relocate one voltmeter).
- Wire to change the inputs “L, M, N, O, P, Q, R, S, T, U, V, W, X, Y, and Z” between -5±1V and 12±1V.
#### Test Procedure
Rewrite for using comparitor out
1) Set up the circuit as shown in the circuit diagrams.
2) For each test change the voltage at the encoder inputs to the specified value, using the +12V and -5V output by the power supply.
3) Measure and record the outputs E, D, C, B, and A.
4) Repeat step 2 to 3 for every test in the test table.
#### Test Review

### Seven Segment Display Sub-System
The Seven Segment Display Sub-System displays a visual representation of BCD signal output by the Priority Encoder Sub-System (page 11) using two seven segment displays.
#### Circuit Diagram
The DS1 display is the 10’s display and DS2 is the units display.

#### Test Diagram
The Test Diagram is the same as the Circuit Diagram, because the visual output of the seven segment displays are being used in testing rather than voltages.
#### Test Table
Test Number	BCD In / V					Expected Display	Observed Display
	E	D	C	B	A
1	0	0	0	0	0	00	00
2	0	0	0	0	5	01	01
3	0	0	0	5	0	02	02
4	0	0	0	5	5	03	03
5	0	0	5	0	0	04	04
6	0	0	5	0	5	05	05
7	0	0	5	5	0	06	06
8	0	0	5	5	5	07	07
9	0	5	0	0	0	08	08
10	0	5	0	0	5	09	09
11	5	0	0	0	0	10	10
12	5	0	0	0	5	11	11
13	5	0	0	5	0	12	12
14	5	0	0	5	5	13	13
15	5	0	5	0	0	14	14
16	5	0	5	0	5	15	15

#### Test Equipment
- Power supply.
- Jumper wires x 5
#### Test Procedure
1) Create the circuit shown as shown in the Test Diagram.
2) Turn off the power supply.
3) Connect the inputs “E, D, C, B, and A” to either 0V or 5V with jumper wires depending on the current test.
4) Turn on the power supply.
5) Look at the displays and record the displayed value.
6) Repeat steps 2 to 5 for each test in the test table.
#### Test Review
Went well, initially had trouble remembering which wires corresponded to which inputs.
On test 5 accidentally connected D3 to 5V instead of D2, this just caused it to display an 8.
## Alternative Sub-Systems
### Analogue In
An alternative design for the Analogue Input Sub-System on page 2 is to create a voltage divider by using a two resistors, with the variable resistor connected to -5V and the resistor connected to 0V.
#### Circuit Diagram

#### Predicted Behaviour
This alternate sub-system would also meet the requirements outlined in the Test Table for the Analogue Input Sub-System (on page 2).
The minimum “Analogue Output” is when the variable resistors (VR1 and VR2) are at their lowest value. Assuming that this is 0Ω, then the minimum output voltage will be -5V, as there is no voltage drop over VR1/VR2, as they have 0 resistance.
To achieve the maximum “Analogue Output” outlined in the Test Table, the value of VR1 and VR2 must be at least 49KΩ. This value was derived from application of the voltage divider formula.
V_{ out } = frac { R_2 times V_{"in"} } { R_1 + R_2 } "=>" R_1 = frac { R_2 times V_{"in"} } { V_{out} } "" - R_2 = frac { 1000 times -5 } { -0.1 } "" - 1000 = 49 times 10^{3}Ω
(The value of -0.1 is the minimum voltage threshold that will still pass the requirements).
The closest value in the E24 series to 49KΩ is 51KΩ. Which will cause an output of -0.096V.
V_{ out } = frac { R_2 times V_{"in"} } { R_1 + R_2 } = frac { 1000 times -5 } { 1000 + 51000 } = -0.096V
#### Disregarding Rational
The main reason for disregarding this variant of the Analogue Input, is because it uses an extra two components compared to the chosen Analogue Input Sub-System. Furthermore, it is not possible for the maximum V_out to ever be 0, unless the maximum resistance of the variable resistor is infinity large. (At least when using the voltage divider equation to predict the output).
### Priority Encoder Output A
For Priority Encoder Sub-System Output A (page 11), I could have made Output A using only NAND gates, rather than including OR gates.
#### Circuit Diagram

#### Predicted Behaviour
This circuit would have behaved identical to the current implementation, as both produce the exact same logical output ( A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M ) for given inputs. Furthermore, since both circuits operate on discrete logic values, any small variance between the circuits will be insignificant.
#### Disregarding Rational
This design was disregarded due to the larger number of logic gates used than in the finial design. This had an even larger impact when constructing the circuit, as I have quad NAND and quad OR integrated circuit chips available to me.
In this alternate design, 28 NAND gates are used, therefore I would have had to use 28 div 4 = 7 quad NAND chips to build this circuit.
The finial design only uses 19 NAND and 3 OR gates, which only needs:
- 19 div 4 = 4.75 (rounded up to 5) NAND chips.
- 3 div 4 = 0.75 (rounded up to 1) OR chip.
To build the circuit, which totals to 5 + 1 = 6 integrated circuits, which is one less than the alternate design. This makes the finial design cheaper and easier to build, write, and test.
### Priority Encoder Binary
This is the previous design of the Priority Encoder Sub-System (on page 11), where a binary signal was output rather than a BCD signal. The binary output was going to be converted into a BCD signal by an SN74184 chip to produce an input for the Seven Segment Display Sub-System (on page 16).
#### Circuit Diagram
##### Output D
##### Output C
##### Output B
##### Output A
An interesting coincidence is that the boolean expression for output “A” is identical between both the BCD and binary design. Therefore, the circuit design for output “A” has not changed. The circuit diagram can be seen at Output A on page 13.
#### Predicted Behaviour
This design of the priority encoder would have worked as expected, as the boolean expressions derived from the truth table produce the at-the-time expected output for the given input. Furthermore, the same logic gates are used in both the Priority Encoder Sub-System and the Priority Encoder Binary, resulting in the behaviour of both circuits being similar, except for the outputs.
##### Truth Table
Encoder In / V					Binary Out / V
L	M	N	O	P	Q	R	S	T	U	V	W	X	Y	Z		D	C	B	A
-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	0
12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	0	5
12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	0
12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	0	5	5
12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	5	0	0
12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	5	0	5
12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5	-5		0	5	5	0
12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5	-5		0	5	5	5
12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5	-5		5	0	0	0
12	12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5	-5		5	0	0	5
12	12	12	12	12	12	12	12	12	12	-5	-5	-5	-5	-5		5	0	5	0
12	12	12	12	12	12	12	12	12	12	12	-5	-5	-5	-5		5	0	5	5
12	12	12	12	12	12	12	12	12	12	12	12	-5	-5	-5		5	5	0	0
12	12	12	12	12	12	12	12	12	12	12	12	12	-5	-5		5	5	0	5
12	12	12	12	12	12	12	12	12	12	12	12	12	12	-5		5	5	5	0
12	12	12	12	12	12	12	12	12	12	12	12	12	12	12		5	5	5	5
Overflow

##### Boolean Expressions
These are the boolean expressions that I derived for the binary outputs:
D = S
C = O. bar S + W
B = Y + U.bar W + Q.bar S + M.bar O
A = Z + X.bar Y + V.bar W + T.bar U + R.bar S + D.bar Q + N.bar O + L.bar M
#### Disregarding Rational
This design had to be replaced by the new Priority Encoder Sub-System, because I was not able to acquire the required chip (SN74184), which would have done the conversion from binary to BCD, due to supply shortages.
Because of this I had to redesign this sub-system to output a BCD signal, making the binary to BCD conversion (and therefore the unavailable chip) redundant.
## System Realisation
The user guide should be “sharp and sweet”. Detailed enough that someone with no experience can use the circuit, but don’t go into detail about the inner workings.
### Circuit Diagram
High Quality labelled block and circuit diagram, including equipment
### Circuit Layout
Include picture of finial circuit?
### Testing
Test Procedures for the entire circuit
During testing, I did not have access to “push-to-break” switches, as specified in the Analogue Input Sub-System (page 2). Therefore, I replaced “break one” and “break two” with “push-to-make” switches.
For tests where the switches are closed, I replaced these switches with orange jump wires to emulate the behaviour of the “push-to-break” switches.
#### Test Tables
##### Table One
Testing switches
Test Number	Test Description	Expected Behaviour	Observed Behaviour
1	Observing the output of the circuit when both analogue input switches are open.	The circuit will output 0.	The circuit output 0.
2	Observing the output when the analogue input one switch is closed.	The circuit will output 5.	The circuit output 5.
3	Observing the output when the analogue input two switch is closed.	The circuit will output 5.	The circuit output 5.
4	Observing the output when the analogue input one switch is closed.	The circuit output 10.	The circuit output 10.

##### Table Two
Testing min and max output
Test Number	Test Description	Expected Behaviour	Observed Behaviour
5	Observing the minimum value displayed by the circuit.	The minimum value displayed value will be 0, at a Vref of 0V.	The minimum value is 0, and the Vref is at 0V.
6	Observing the maximum value displayed by the circuit.	The maximum displayed value will be 15, at a Vref of 9.15V.	The maximum displayed value is 15, and the Vref is as.

##### Table Three
Test Number	Previous Number	Current Number	Expected Previous	Expected Number
7	N/A	0	N/A	0
8	0	1	0	1
9	1	2	1	2
10	2	3	2	3
11	3	4	3	4
12	4	5	4	5
13	5	6	5	6
14	6	7	6	7
15	7	8	7	8
16	8	9	8	9
17	9	10	9	10
18	10	11	10	11
19	11	12	11	12
20	12	13	12	13
21	13	14	13	14
22	14	15	14	15

#### Test Procedure
Quoted words are terms referring to the Analogue Input Sub-System (page 2).
0) Before each test, ensure that the circuit is set up the circuit as shown in the Circuit Diagram (page 22).
##### Table One
1) Change “break one” to be open and “break two” to be closed. Then adjust “VR1” so that it gives a display output of 5.
2) Without changing the value of “VR1”, swap “break one” to be closed and “break two” to be open. Then adjust “VR2” so that it also gives a display output of 5.
3) Do not adjust the value of “VR1” and “VR2” for the remained of this test block.
4) For test 1, measure and record the displayed output when both “break one” and “break two” are open.
5) For test 2, measure and record the displayed output when “break one” is closed and “break two” is open.
6) For test 3, measure and record the displayed output when “break one” is open and “break two” is closed.
4) For test 4, measure and record the displayed output when both “break one” and “break two” are closed.
##### Table Two
1) Ensure that both “break one” and “break two” are closed.
2) For test 5, change both the potentiometers “VR1” and “VR2” to their lowest value, then measure and record the displayed value.
3) ...
##### Table Three
During tests 1, 2, 3, and 4, the Analogue inputs have a logical value of 5.
test 5: Both A in have a value of 0 and Vref is at 0V (measured)
test 6:
### Test Analysis
##### Table One
Test table one tests the ability of the circuit to display values individually, and combined.
The tests for table one (1 to 4), went well. Tests 1, 2, and 3 all passed without any issues. Test 4 occasionally gave an output of 11. However, I believe that this was due to the true value of each analogue input being above 5.5, whilst being bellow 6. This will cause the combined output to correctly display 11, as 5.5 + 5.5 = 11 .
I can get the test to consistently pass by ensuring that both inputs were at the lower range of the output value 5.
##### Table Two

##### Table Three
Test table three tests the ability of the circuit to count consecutively up to 15 from 0.
The tests for table three (7 to 22) went very well. With each number correctly increasing by one to the higher number.
Some flickering between numbers can be observed if the boundary between two numbers if the user slowly adjusts the analogue inputs. However, this flickering does not impact the tests, as the output flickers between the previous and next number.
### Interfacing sub-systems
#### Priority Encoder and Seven Segment Display
When I was connecting the output of the Priority Encoder Sub-System (page 11) to the input of the Seven Segment Display Sub-System (page 16) I also had to connected the Seven Segment Display to +5V and to 0V, which I initially took from the Priority Encoder.
However, during testing I found that the +5V wires for the Priority Encoder could drop to as low as 2.5V at when Vref is at a low value. This caused the Seven Segment Displays to flicker or even turn off.
To solve this, I changed the wiring to so that the Seven Segment Display is getting +5V and 0V from the main board, rather than the from the Priority Encoder.
After making this change, the Seven Segment Displays illuminated consistently and brightly while the Priority Encoder has a low Vref input.
#### Mixer and Comparator Chain
Mixer vout originally negative, changed A in to use -V instead of +V to fix the issue.
### User guide
A guide on how to use the entire circuit.
## Evaluation
Improvements:
Add resistors between Comparator chain and priority encoder, because the comparators/op amps get very hot.
Connect the overflow output from the ADC to the seven seg driver to make them blank/8 when overflow (include about clamping voltage to correct range).